## Slide 1: Shining Through: Net Load Forecasting in Solar-Rich South Australia
An industry project for TESLA Asia Pacific
By: Chase Robertson Supervisor: Simon Urbanek
Notes: Hello, I’m Chase Robertson, and with guidance from Simon Urbanek, researched net load forecasting in solar-rich South Australia for Tesla Asia Pacific.

## Slide 2: Introduction
Wind turbines, solar panels, high-capacity home batteries, oh my!
Electricity markets are changing; distributed generation is on the rise.
Electricity demand is less predictable when consumers also produce electricity behind-the-meter.
This Photo from Wikipedia is licensed under CC BY-SA
Notes: Wind turbines, solar panels, high-capacity home batteries, oh my! Electricity markets are changing: distributed generation is on the rise.
Back in the good old days, consumers of electricity would only consume, so producers could forecast future demand based on patterns of past demand, and a bit of intuition about upcoming social conditions, and how those might affect demand.
Nowadays, consumers are also producers, especially when the sun is shining, and most especially in sunny areas like South Australia, where 40% of homes have rooftop solar systems! This complicates matters and makes weather a much more important factor in demand prediction.
So, we call the amount of electricity drawn from the GRID across a region “net load” and want to know how best to forecast this load over the next 24-48 hours under these new solar-rich conditions.

## Slide 3: Load in Australia
Notes: Let’s have a look at the average daily profiles for each year of our load data from New South Wales and South Australia. Of course, these averaged profiles paint a very rosy picture of reality. Any given individual day shows much greater variance in demand.
That said, notice the unchanged base load at the x-axis extremes, and contrast that with the deepening mid-day dip over the years – the change due to increased solar generation. It’s a great change in both cases, but having a look at the y-axis values, its proportionally most significant in South Australia.

## Slide 4: Existing Methods
Generalised Additive Mixed Models (GAMM)
Fit 2014 NSW weekdays with an R2 of 0.89
Using only day-of-year, time-of-day, and time-weighted-temperature. Parsimonious!
Notes: Past research into modelling Australian demand for electricity utilised a parsimonious Generalised Additive Mixed Model, or GAMM, which fit NSW data well enough using only:
Day of the year (top figure - winter and summer induce more demand)
Time of the day (middle figure - inclusive of Daylight Savings shifts to more precisely reflect consumer activity)
Temperature (bottom figure - weighted by time of day, because people tend not to care as much about outside temperatures when they’re bundled up dreaming about their low electricity bill and care a lot more when they’re up and about.)
That’s all well and good, but we wondered: with how non-linear demand tends to be in reality, how would non-linear models fare?

## Slide 5: Methodology
How much data should be used, given so much change?
How accurate are long forecasts, given ”perfect” knowledge of weather?
How can holidays be addressed?
Notes: Additionally, we wanted to test the actual accuracy of forecasts, rather than just the closeness of fit, as previous research had focussed on, which opened up a new set of methodological questions:
If demand patterns are changing, how much data should be used to train a model? Will data from three years ago be helpful or detrimental? How different are the results from fixed-width sliding training windows versus expanding windows of training data?
If our task is predicting the next 24-48 hours, but we have perfect knowledge of the weather conditions, how different would extended forecasting accuracy be?
It’s well-known in the industry that holidays tend to be more difficult to forecast, so how can holiday information be included to best improve accuracy?

## Slide 6: Performance
Model | MAE | MAPE (%) | RMSE
Parsimonious GAMM | 142 | 13.4 | 180
GAMM + solar irradiance | 114 | 10.1 | 149
GAMM + all weather variables | 115 | 10.3 | 148
GAMM + irradiance -> Residual RF | 104 | 9.3 | 137
Random Forest | 94 | 8.7 | 129
HGB with binary holidays | 93 | 8.4 | 134
Tuned HGB with AEMO Solar Estimate | 65 | 5.8 | 84
Notes: So we experimented!
We added weather terms to the GAMM baseline model, including measured solar irradiance, which was a big help, and tried modelling the residuals from each GAMM with a Random Forest. We also tried applying Random Forest (RF) and Histogram Gradient Boosting (HGB) ensemble models directly to the data and found that those forecasts were more accurate.
In addition, we included solar generation estimates from the actual grid managers: the Australian Energy Market Operator (AEMO). These may not be available in other countries but were hugely helpful in increasing accuracy.
We found that HGB predicted most accurately among the attempted models.

## Slide 7: Prediction
Histogram Gradient Boosting (HGB)
Low learning rate
High number of iterations (trees)
Notes: By tuning the HGB hyperparameters, we found that slow, deep training resulted in the best accuracy.
Here we show an example of net load prediction from an HGB model. This particular day is quite different from the average profiles shown earlier, not so smooth, but the model does a pretty good job of forecasting the demand.

## Slide 8: Conclusion
We found that an HGB with 1-2 years of training data and binary holiday encoding forecasted best.
Future work could benefit from:
- Data from more weather sites
- Separate physics-based solar modelling
- More complex hybrid techniques
Notes: In conclusion, we were able to explore the methodological space and decide that annual to bi-annual training windows with binary holiday encoding resulted in the best prediction.
By sacrificing a bit of parsimony and going beyond time-series modelling techniques, we were able to forecast more accurately using our ensemble models, achieving as low as 6% Mean Absolute Percentage Error (the most common metric for comparing inter-regional performance).
Future work in this context will likely find further success by:
Incorporating data from more weather sites (we used just one weather station in the most populous city, Adelaide)
Modelling the maximum solar contribution separately based on physical limits
Exploring multi-model hybrid techniques like our residual modelling attempt, but with more complex models

## Slide 9: References
Electricity Meter Image: https://commons.wikimedia.org/wiki/File:Hydro_quebec_meter.JPG
GAMM: J. McCulloch and K. Ignatieva, “Intra-day electricity demand and temperature,” The Energy Journal, vol. 41, no. 3, 2020.
Sliding/Expanding Window Figures:
https://www.uber.com/en-NZ/blog/omphalos/

## Slide 10
Thank you